## Slide 1: Capital Trade-Offs
Evaluated three major capital expenditure scenarios
  Speed and Reliability Corridor Improvements
  Direct Access Ramp Improvements
  Park and Ride Expansion

## Slide 2: Speed and Reliability Improvements
About 240 miles of Speed and Reliability Improvements
Focused on 2040 network frequent/very frequent transit corridors
Assumed 15 percent improvement in travel speeds over baseline conditions
No specific improvements identified (TSP, BAT lanes, etc.)
Cost assumed at $2.0M per mile (based on TCRP research)
Assumes new Ship Canal Crossing at $100M with bus lanes
Notes: TRCP research identified bus S&R improvements at $2.7M per mile. Assumes that 75 percent of network needs this high level of investment

## Slide 3: Direct Access Ramps
Assumed five new direct access ramp projects
  SODO Busway to Seattle Blvd/Airport Way
  West Seattle Freeway to 1st Avenue S/SR 99
  I-5 to Industrial Way/SODO Busway
  I-5 to SR 900
  SR 167/James St
These ramps are in addition to the I-405 Corridor Master Plan ramps
Ramps assumed to cost $96M each, mid-range price of I-405 ramp project cost estimates
Each ramp reduces transit route travel time by 4-6 minutes
Notes: The ramp projects were originally identified to serve the Express Concept Network. If we were to pursue the ramps for the Draft Preferred Network, then we would select other ramps since some of the ramps listed above do not have much usage in the new network

## Slide 4: Park and Ride Expansion
Double the number of publicly owned park-and-ride spaces (20,500 to 41,000 stalls)
Assumed to be located at existing high-utilization lots
Mix of surface lots and garages
$30,000 per stall
Notes: The ramp projects were originally identified to serve the Express Concept Network. If we were to pursue the ramps for the Draft Preferred Network, then we would select other ramps since some of the ramps listed above do not have much usage in the new network

## Slide 5: Impacts: Boardings and Rev. Hours
Scenario | Change in Daily Boardings |  | Change in Annual Revenue Hours with Improvement | 
 | Total | Percent | Total | Percent
Speed and Reliability Improvements | +47,300 | 4.9% | -228,942 | -5.1%
Direct Access Ramps | +13,000 | 1.4% | -70,840 | -1.5%
Park-and-Ride Expansion | +42,000 | 4.6% | N/A | 
Notes: Reformatted slide to show the increase in ridership from the improvement and the reduction in revenue hours if the improvement was in place. Note that we do not assume any rerouting impacts from the expanded park and rides.

## Slide 6: Capital Improvements: Total Costs
Scenario | Total Costs
Speed and Reliability Improvements | $574 million
Direct Access Ramps | $480 million
Park-and-Ride Expansion | $615 million

## Slide 7: Payback and Amortization Assumptions
Cost per revenue hour: $161 (based on 2014 data from Metro)
Interest rate: 5%
Lifespan of capital investments (amortization period): 50 years
  Assumes the bulk of the improvements have long life spans
Average fare per boarding: $1.24 (based on 2014 data from Metro)
Notes: The ramp projects were originally identified to serve the Express Concept Network. If we were to pursue the ramps for the Draft Preferred Network, then we would select other ramps since some of the ramps listed above do not have much usage in the new network

## Slide 8: Payback Period and Annual Cost per Rider
Scenario | Payback Period | Annualized Capital Cost per Annual Boarding | Benefit/Cost Ratio
Speed and Reliability Improvements | 6 years | $2.10 | 1.77
Direct Access Ramps | 29 years | $6.30 | 0.63
Park-and-Ride Expansion | 36 years | $2.50 | 0.49
Notes: Payback period = total capital cost/annual fares and revenue hour savings
Annualized Capital Cost per Annual Boarding= Annualized cost of the investment / new annual boardings resulting from the improvement
Benefit/cost ration = annual benefit (including fares and revenue hours savings)/annualized capital cost
* Note that we do not assume maintenance costs in any of these calculations

## Slide 9: Findings
Speed and reliability improvements are the most cost effective type of capital improvement
  Combination of high ridership and service hours savings
  Only type of improvement with a positive benefit/cost ratio
Direct access ramps have a high annualized cost per annual boarding, but provide service hours savings, offsetting the cost somewhat
Park-and-ride stalls generate riders and fares, but have the lowest benefit/cost ratio (this could change if parking is not free)
Notes: The ramp projects were originally identified to serve the Express Concept Network. If we were to pursue the ramps for the Draft Preferred Network, then we would select other ramps since some of the ramps listed above do not have much usage in the new network